## Slide 1: Preventing Page Faults from Telling Your Secrets
Shweta Shinde Zheng Leong Chua
Vishwesh Narayanan Prateek Saxena
National University of Singapore

## Slide 2: Should user application trust the OS?
Operating
Systems
Hypervisor
CVEs in Linux [CVE-DB]
CVEs in Xen [CVE-DB]
150 KLOC
10 MLOC
Large TCB
Increases the risk of
rootkits and malware

## Slide 3: Hardware Isolated Enclaves
OS cannot access application’s memory
Long line of work: Overshadow, Inktag, AppShield, PodArch, Intel SGX, ….
CPU
Untrusted OS
From October 2015, Intel has started shipping SGX support in commodity Skylake Processors
Intel SGX
Enclaves

## Slide 4: Problem in the Design of Enclaves
OS manages enclave resources
Opens attack surface via side channels: system calls, file I/O
Recent attack channel: Page Fault*
Memory management
Intel SGX CPU
*[Xu et al. – IEEE S&P’15]

## Slide 5
Are security critical cache-hardened applications vulnerable?

## Slide 6: A Real Example: AES Encryption
Enclave
Intel SGX CPU
Table 1 [1c], …, Table1[ff]
Enclave’s pages
Application page table
Page faults:
Virtual Memory
mov Table1[idx], rax
Table 1 [0], …, Table 1 [1b]
P0
P1
P2
P2
P1
P1
P2
3E
1A
09
46
idx:
Leaks 25 bits of encryption key in first round!
“Pigeonholes”
Page Accesses
Physical Memory
Table 1 [0], …, Table 1 [1b]
Table 1 [1c], …, Table1[ff]
Notes: Severity and defense

## Slide 7: Contributions
Attacks on real crypto routine implementations
Technique to eliminate page fault side-channel
Hardware changes for lowering the overheads
10 / 24
are vulnerable
Leak 27 bits
on average
Compiler support
for annotations
Performance
Optimization

## Slide 8: Pigeonhole Attack Example: Data Access
mov Table1[idx], rax
idx < 1c
idx >= 1c
P1
P2
Table 1
Input dependent data page access leaks
25 bits of information
Notes: OS cannot directly access to program memory

## Slide 9: Pigeonhole Attack Example: Code Access
ec_mul
P1:
0xA7310
add_points
P2:
0xA6CB0
test_bit
P3:
0x9EB30
ec_mul(r, G) {
res = O
nbits = |r|
for (i = nbits-1; i>=0; i--):
res = dup_point(res)
if (test_bit(r[i])):
res = add_points(res, G)
return res }
r[i]==1
r[i]==0
Input dependent code page access reveals
all the bits of ECDSA keys!
ECDSA Signing Routine

## Slide 10: Impact of Pigeonhole Attacks
Analyzed Libgcrypt v1.6.3, OpenSSL v1.0.2
  Compiled with gcc v4.8.3 and LLVM v3.4
Leakage via input dependent data page access
  AES, CAST5, SEED, Stribog, Tiger, Whirlpool
Leakage via input dependent code page access
  EdDSA, powm (used by RSA, DSA, ElGamal)

## Slide 11: Impact of Pigeonhole Attacks
OS can infer significant number of bits

## Slide 12
Defenses against Pigeonhole Attacks

## Slide 13: A Software-only Defense: Determinising Page Accesses
Observation:
OS cannot differentiate accesses in a page
Key Insight:
Confine all input-dependent memory accesses to a staging page
Program will exhibit same page-access profile independent of the input
Make the program execution Page-fault Oblivious

## Slide 14: Solution Overview
Program
Source
Code
Developer
Annotations
Rewrite
Program Instructions
Identify Sensitive
Code & Data
PF-Oblivious
Program
Input
Enforce Deterministic Page Accesses
Output
Determinise
Page Layout

## Slide 15: Determinising Page Layout
Enclave’s
Staging Page

## Slide 16: Multiplexed Execution
Fetch all the input-dependent code / data to a staging page
Execute the dependent-logic within the staging page via a multiplexer
Save the updated values from data page

## Slide 17: Example: Determinising Data Accesses
P1
P2
Table 1
mov Table1[idx],rax
P0
P0: Code
Staging Page
mov Table1[idx],rax
P0 P1 P0 P2 P0 P1 P0 P2
Page-fault
Profile:
Table 1
P1: Data
Staging Page
P0 P1 P0 P1 P0 P1 P0 P1
Page-fault
Profile:

## Slide 18: Example: Determinising Code Accesses
P0: Code
Staging Page
P1 P2 P1 P3 P1
Page-fault
Profile r =1
P1: Data
Staging Page
P0 P1 P0
Page-fault
Profile:
ec_mul
P1:
0xA7310
add_points
P2:
0xA6CB0
test_bit
P3:
0x9EB30
ec_mul
add_points
test_bit
r[i]==1 or 0
P1 P2 P1 P3 P1 P1 P2
Page-fault
Profile r =0

## Slide 19: More Complex Example: powm
powm
mul_mod
karatsuba_release
set_cond
karatsuba_case
mpih_divrem
mpih_mul
mul_N, mul_N_basecase
Arithmetic Operations (addition, subtraction, shift)
Enclave’s
Staging Page

## Slide 20
Performance Evaluation
*All measurements were conducted on PodArch [NUS-TR]

## Slide 21: Evaluation: Unoptimized Overhead
Fetch-Save Operations Dominate the Costs
Directly enforcing deterministic multiplexing is costly

## Slide 22
Incurs huge overhead for real programs
(> 4000X for powm)

## Slide 23: Optimizations: Exploiting Data Locality
O1: Eliminating copy operations
Skip the save operation for read-only data
O2: Page Realignment
Merge small data blocks into a single page
Reduces fetch operations

## Slide 24: Optimizations: Exploiting Code Locality
O3: Level Merging
mul_mod
karatsuba_case
mpih_divrem
mpih_mul
mul_N, mul_N_basecase
Arithmetic Operations (addition, subtraction, shift)
Enclave’s
Staging Page

## Slide 25: Optimizations: Exploiting Code Locality
O4: MUX Elimination, no staging area
mul_mod
karatsuba_case
mpih_divrem
mpih_mul
mul_N, mul_N_basecase
Arithmetic Operations (addition, subtraction, shift)
Code Page 1
Code Page 2

## Slide 26: Optimizations: Exploiting Code Locality
O5: Control-to-Data Dependency Transformation (if-conversion)
if (c) {
result = result*2;
}
staging_area[0] = result;
staging_area[1] = result*2;
result = staging_area[c];
Input-dependent code access
Input-dependent data access

## Slide 27: End-to-end Solution
Program
Source
Code
Developer
Annotations
Rewrite
Program Instructions
Identify Sensitive
Code & Data
PF-Oblivious
Program
Input
Output
Determinise
Page Layout
Developer Optimization
Implemented as Clang-LLVM Compiler Pass

## Slide 28: Evaluation: Effectiveness of Optimizations
Case-Specific Optimizations Are Orders of Magnitude Better!

## Slide 29
Hardware-based Solution

## Slide 30: Hardware Approach: Contractual Execution
Sensitive Computation
Enclave
Page Contract: {P1, P2, P3}
Enclave Fault Handler:
get TIME
wait (TIME- k)
terminate ()
OS
CPU
Page
Fault
Abort
Enclave
Request
Register

## Slide 31: Potential Hardware Changes
  Inform enclave about the page-fault
    Support available in SGX v2
  Establishing and enforcing contracts
    Requires additional hardware support
Implemented as amendments to PodArch

## Slide 32: Evaluation: Hardware-based Solution Overhead
A Simpler Defense with 7% overheads is possible with a hardware modification!

## Slide 33: Related Work
Oblivious RAM
Self-paging
Cache
Hardening
Time
Bucketing
Notes: Cache hardening
ORAM

## Slide 34: Conclusion
Attacks on OpenSSL and Libgrcypt implementations
Software defense by determinzing page faults
Hardware approach reduces overhead to 6.77%
10 / 24
are vulnerable
27-100 %
leakage
Compiler support
for annotations
Max. 29.22% opt. overhead

## Slide 35: Intel’s Note for Enclave Programmers

## Slide 36: Contact
Shweta Shinde
shweta24@comp.nus.edu.sg
Thank You !

## Slide 37: References
[CCS’15] Y. Xu, W. Cui, and M. Peinado, Controlled-Channel Attacks: Deterministic Side Channels for Untrusted Operating Systems
[OSDI’14] A. Baumann, M. Peinado, G. Hunt, Shielding Applications from an Untrusted Cloud with Haven.
[HASP’13] F. McKeen, I. Alexandrovich, A. Berenzon, C. V. Rozas, H. Shafi, V. Shanbhogue, U. R. Savagaonkar, Innovative Instructions and Software Model for Isolated Execution
[S&P’15] Shweta Shinde, Shruti Tople, Deepak Kathayat, Prateek Saxena, Poster: PodArch: Protecting Legacy Applications with a Purely Hardware TCB
[JACM ‘96] O. Goldreich and R. Ostrovsky, Software Protection and Simulation on Oblivious RAMs
Software Guard Extensions Programming Reference Rev. 2 software.intel.com/sites/default/files/329298-002.pdf
Intel® Software Guard Extensions Enclave Writer’s Guide https://software.intel.com/sites/default/files/managed/ae/48/Software-Guard-Extensions-Enclave-Writers-Guide.pdf

## Slide 38
Backup Slides

## Slide 39: If staging area doesn’t fit in page?
Compacted Multiplexing with Smart Copy:
While fetching, keep over-writing the fake blocks
Copy real block in non-overlapping location in the page
OS cannot see that the copy within a page is overwriting the content

## Slide 40: AES: Information Leakage Calculations
AES first round uses the first 128 bits of the key
Initial uncertainty = 2128
OS knows for half the bits
  if the index is less than 0x1c (28 8-bit values)
Final uncertainty = 264 × 288
Information leakage (in bits)
log2(2128− (264 × 288))
  = 25.54 bits

## Slide 41: Timing Channel
Crypto implementations have balanced execution trees
If the adversary can distinguish executions in the PF-oblivious execution, then he can learn that information even in absence of PF-channel